## Slide 1: Digital Design & Computer Arch. Lecture 8: Timing and Verification
Prof. Onur Mutlu
ETH Zürich
Spring 2020
13 March 2020

## Slide 2: Required Readings (This Week)
Hardware Description Languages and Verilog
  H&H Chapter 4 in full
Timing and Verification
  H&H Chapters 2.9 and 3.5 + (start Chapter 5)
By tomorrow, make sure you are done with
  P&P Chapters 1-3 + H&H Chapters 1-4

## Slide 3: Required Readings (Next Week)
Von Neumann Model, LC-3, and MIPS
  P&P, Chapter 4, 5
  H&H, Chapter 6
  P&P, Appendices A and C (ISA and microarchitecture of LC-3)
  H&H, Appendix B (MIPS instructions)
Programming
  P&P, Chapter 6
Recommended: Digital Building Blocks
  H&H, Chapter 5

## Slide 4: What Will We Learn Today?
Timing in combinational circuits
  Propagation delay and contamination delay
  Glitches
Timing in sequential circuits
  Setup time and hold time
  Determining how fast a circuit can operate
Circuit Verification
  How to make sure a circuit works correctly
  Functional verification
  Timing verification

## Slide 5: Tradeoffs in Circuit Design

## Slide 6: Circuit Design is a Tradeoff Between:
Area
  Circuit area is proportional to the cost of the device
Speed / Throughput
  We want faster, more capable circuits
Power / Energy
  Mobile devices need to work with a limited power supply
  High performance devices dissipate more than 100W/cm2
Design Time
  Designers are expensive in time and money
  The competition will not wait for you

## Slide 7: Requirements and Goals Depend On Application

## Slide 8: Circuit Timing
Until now, we investigated logical functionality
What about timing?
  How fast is a circuit?
  How can we make a circuit faster?
  What happens if we run a circuit too fast?
A design that is logically correct can still fail because of real-world implementation issues!

## Slide 9: Part 1: Combinational Circuit Timing

## Slide 10: Digital Logic Abstraction
“Digital logic” is a convenient abstraction
  Output changes immediately with the input
A
Y
1
0
0
1

## Slide 11: Combinational Circuit Delay
In reality, outputs are delayed from inputs
  Transistors take a finite amount of time to switch
time

## Slide 12: Real Inverter Delay Example
Image source: Sandoval-Ibarra, F., and E. S. Hernández-Bernal. "Ring CMOS NOT-based oscillators: Analysis and design." Journal of applied research and technology, 2008.

## Slide 13: Circuit Delay and Its Variation
Delay is fundamentally caused by
  Capacitance and resistance in a circuit
  Finite speed of light (not so fast on a nanosecond scale!)
Anything affecting these quantities can change delay:
  Rising (i.e., 0 -> 1) vs. falling (i.e., 1 -> 0) inputs
  Different inputs have different delays
  Changes in environment (e.g., temperature)
  Aging of the circuit
We have a range of possible delays from input to output

## Slide 14: Delays from Input to Output
Contamination delay (tcd): delay until Y starts changing
Propagation delay (tpd): delay until Y finishes changing
Example Circuit
Effect of Changing Input ‘A’
Cross-hatching
means value is changing

## Slide 15: Calculating Long/Short Paths
Critical (Longest) Path: tpd = 2 tpd_AND + tpd_OR
Shortest Path: tcd = tcd_AND
We care about both the longest and shortest paths in a circuit (we will see why later in the lecture)

## Slide 16: Example tpd for a Real NAND-2 Gate
Heavy dependence on voltage and temperature!
Source: Nexperia 2-input NAND (74HC00) Datasheet, Section 10

## Slide 17: Example Worst-Case tpd
Two different implementations of a 4:1 multiplexer
Gate Delays
Implementation 1
Implementation 2
Different designs lead to very different delays

## Slide 18: Disclaimer: Calculating Long/Short Paths
It’s not always this easy to determine the long/short paths!
  Not all input transitions affect the output
  Can have multiple different paths from an input to output
In reality, circuits are not all built equally
  Different instances of the same gate have different delays
  Wires have nonzero delay (increasing with length)
  Temperature/voltage affect circuit speeds
    Not all circuit elements are affected the same way
    Can even change the critical path!
Designers assume “worst-case” conditions and run many statistical simulations to balance yield/performance

## Slide 19: Combinational Timing Summary
Circuit outputs change some time after the inputs change
  Caused by finite speed of light (not so fast on a ns scale!)
  Delay is dependent on inputs, environmental state, etc.
The range of possible delays is characterized by:
  Contamination delay (tcd): minimum possible delay
  Propagation delay (tpd): maximum possible delay
Delays change with:
  Circuit design (e.g., topology, materials)
  Operating conditions

## Slide 20: Output Glitches

## Slide 21: Glitches
Glitch: one input transition causes multiple output transitions
Circuit initial state
1
1
0
0

## Slide 22: Glitches
0
1
1 -> 0
1 -> ?
Glitch: one input transition causes multiple output transitions

## Slide 23: Glitches
0
1
1 -> 0
1 -> ?
Slow path (3 gates)
Fast path (2 gates)
Glitch: one input transition causes multiple output transitions

## Slide 24: Glitches
0
1
1 -> 0
1 -> 0 -> 1
Slow path (3 gates)
Fast path (2 gates)
Glitch: one input transition causes multiple output transitions

## Slide 25: Glitches
0
1
(B) 1 -> 0
(Y) 1 -> 0 -> 1
Slow path (3 gates)
Fast path (2 gates)
n1
n2
Glitch: one input transition causes multiple output transitions

## Slide 26: Avoiding Glitches Using K-Maps
Glitches are visible in K-maps
  Recall: K-maps show the results of a change in a single input
  A glitch occurs when moving between prime implicants
(A) 0
(C) 1
(B) 1 -> 0
(Y) 1 -> 0 -> 1
AB
BC

## Slide 27: Avoiding Glitches Using K-Maps
We can fix the issue by adding in the consensus term
  Ensures no transition between different prime implicants
(A) 0
(C) 1
(B) 1 -> 0
(Y) 1 -> 1
AB
BC
AC
No dependence on B
=> No glitch!

## Slide 28: Avoiding Glitches
Q: Do we always care about glitches?
  Fixing glitches is undesirable
    More chip area
    More power consumption
    More design effort
  The circuit is eventually guaranteed to converge to the right value regardless of glitchiness
A: No, not always!
  If we only care about the long-term steady state output, we can safely ignore glitches
  Up to the designer to decide if glitches matter in their application

## Slide 29: Part 2: Sequential Circuit Timing

## Slide 30: Recall: D Flip-Flop
Flip-flop samples D at the active clock edge
  It outputs the sampled value to Q
  It “stores” the sampled value until the next active clock edge
D
Q
CLK
The D flip-flop is made from combinational elements
D, Q, CLK all have timing requirements!

## Slide 31: D Flip-Flop Input Timing Constraints
D must be stable when sampled (i.e., at active clock edge)
D
Q
CLK
Setup time (tsetup): time before the clock edge that data must be stable (i.e. not changing)
Hold time (thold): time after the clock edge that data must be stable
Aperture time (ta): time around clock edge that data must be stable (ta = tsetup + thold)

## Slide 32: Violating Input Timing: Metastability
If D is changing when sampled, metastability can occur
  Flip-flop output is stuck somewhere between ‘1’ and ‘0’
  Output eventually settles non-deterministically
Source: W. J. Dally, Lecture notes for EE108A, Lecture 13: Metastability and Synchronization Failure (When Good Flip-Flops go Bad) 11/9/2005.
CLK
Q
Example Timing Violations (NAND RS Latch)
Metastability
Non-deterministic Convergence

## Slide 33: Flip-Flop Output Timing
Contamination delay clock-to-q (tccq): earliest time after the clock edge that Q starts to change (i.e., is unstable)
Propagation delay clock-to-q (tpcq): latest time after the clock edge that Q stops changing (i.e., is stable)
D
Q
CLK

## Slide 34: Recall: Sequential System Design
Multiple flip-flops are connected with combinational logic
Clock runs with period Tc (cycle time)
Must meet timing requirements for both R1 and R2!

## Slide 35: Ensuring Correct Sequential Operation
Need to ensure correct input timing on R2
Specifically, D2 must be stable:
  at least tsetup before the clock edge
  at least until thold after the clock edge

## Slide 36: Ensuring Correct Sequential Operation
This means there is both a minimum and maximum delay between two flip-flops
  CL too fast -> R2 thold violation
  CL too slow -> R2 tsetup violation
Potential
R2 tHOLD VIOLATION!
Potential
R2 tSETUP VIOLATION!
tHOLD
tSETUP

## Slide 37: Setup Time Constraint
Safe timing depends on the maximum delay from R1 to R2
The input to R2 must be stable at least tsetup before the clock edge.
Tc

## Slide 38: Setup Time Constraint
Tc > tpcq
Safe timing depends on the maximum delay from R1 to R2
The input to R2 must be stable at least tsetup before the clock edge.

## Slide 39: Setup Time Constraint
Tc > tpcq + tpd
Safe timing depends on the maximum delay from R1 to R2
The input to R2 must be stable at least tsetup before the clock edge.

## Slide 40: Setup Time Constraint
Tc > tpcq + tpd + tsetup
Safe timing depends on the maximum delay from R1 to R2
The input to R2 must be stable at least tsetup before the clock edge.

## Slide 41: Setup Time Constraint
Safe timing depends on the maximum delay from R1 to R2
The input to R2 must be stable at least tsetup before the clock edge.
Tc > tpcq + tpd + tsetup
Useful work
Wasted work
Sequencing overhead: amount of time wasted each cycle due to sequencing element timing requirements

## Slide 42: tsetup Constraint and Design Performance
Critical path: path with the longest tpd
Overall design performance is determined by the critical path tpd
  Determines the minimum clock period (i.e., max operating frequency)
  If the critical path is too long, the design will run slowly
  If critical path is too short, each cycle will do very little useful work
    i.e., most of the cycle will be wasted in sequencing overhead
Tc > tpcq + tpd + tsetup

## Slide 43: Hold Time Constraint
Safe timing depends on the minimum delay from R1 to R2
D2 (i.e., R2 input) must be stable for at least thold after the clock edge
tccq
Must not change until thold after the clock

## Slide 44: Hold Time Constraint
tccq + tcd
Safe timing depends on the minimum delay from R1 to R2
D2 (i.e., R2 input) must be stable for at least thold after the clock edge

## Slide 45: Hold Time Constraint
Safe timing depends on the minimum delay from R1 to R2
D2 (i.e., R2 input) must be stable for at least thold after the clock edge
tccq + tcd > thold

## Slide 46: Hold Time Constraint
tccq + tcd > thold
tcd > thold - tccq
We need to have a minimum combinational delay!
Safe timing depends on the minimum delay from R1 to R2
D2 (i.e., R2 input) must be stable for at least thold after the clock edge

## Slide 47: Hold Time Constraint
Safe timing depends on the minimum delay from R1 to R2
D2 (i.e., R2 input) must be stable for at least thold after the clock edge
Does NOT depend on Tc!
tccq + tcd > thold
tcd > thold - tccq
Very hard to fix thold violations after
manufacturing- must modify circuits!

## Slide 48: Sequential Timing Summary
tccq / tpcq | clock-to-q delay (contamination/propagation)
tcd / tpd | combinational logic delay (contamination/propagation)
tsetup | time that FF inputs must be stable before next clock edge
thold | time that FF inputs must be stable after a clock edge
Tc | clock period

## Slide 49: Example: Timing Analysis
Timing Characteristics
tccq = 30 ps
tpcq = 50 ps
tsetup = 60 ps
thold = 70 ps
tpd = 35 ps
tcd = 25 ps
tpd =
tcd =
Check setup time constraints:
Tc > tpcq + tpd + tsetup
Tc >
fmax = 1/Tc =
Check hold time constraints:
tccq + tcd > thold ?

## Slide 50: Example: Timing Analysis
Timing Characteristics
tccq = 30 ps
tpcq = 50 ps
tsetup = 60 ps
thold = 70 ps
tpd = 35 ps
tcd = 25 ps
tpd = 3 x 35 ps = 105 ps
tcd =
Check setup time constraints:
Tc > tpcq + tpd + tsetup
Tc >
fmax = 1/Tc =
Check hold time constraints:
tccq + tcd > thold ?

## Slide 51: Example: Timing Analysis
Timing Characteristics
tccq = 30 ps
tpcq = 50 ps
tsetup = 60 ps
thold = 70 ps
tpd = 35 ps
tcd = 25 ps
tpd = 3 x 35 ps = 105 ps
tcd = 25 ps
Check setup time constraints:
Tc > tpcq + tpd + tsetup
Tc >
fmax = 1/Tc =
Check hold time constraints:
tccq + tcd > thold ?

## Slide 52: Example: Timing Analysis
tpd = 3 x 35 ps = 105 ps
tcd = 25 ps
Check setup time constraints:
Tc > tpcq + tpd + tsetup
Tc > (50 + 105 + 60) ps = 215 ps
fmax = 1/Tc = 4.65 GHz
Timing Characteristics
tccq = 30 ps
tpcq = 50 ps
tsetup = 60 ps
thold = 70 ps
tpd = 35 ps
tcd = 25 ps
Check hold time constraints:
tccq + tcd > thold ?
tpd
tpcq
tsetup

## Slide 53: Example: Timing Analysis
tpd = 3 x 35 ps = 105 ps
tcd = 25 ps
Check setup time constraints:
Tc > tpcq + tpd + tsetup
Tc > (50 + 105 + 60) ps = 215 ps
fmax = 1/Tc = 4.65 GHz
Check hold time constraints:
tccq + tcd > thold ?
(30 + 25) ps > 70 ps ?
Timing Characteristics
tccq = 30 ps
tpcq = 50 ps
tsetup = 60 ps
thold = 70 ps
tpd = 35 ps
tcd = 25 ps
tccq
tcd

## Slide 54: Example: Timing Analysis
tpd = 3 x 35 ps = 105 ps
tcd = 25 ps
Check setup time constraints:
Tc > tpcq + tpd + tsetup
Tc > (50 + 105 + 60) ps = 215 ps
fmax = 1/Tc = 4.65 GHz
Check hold time constraints:
tccq + tcd > thold ?
(30 + 25) ps > 70 ps ?
Timing Characteristics
tccq = 30 ps
tpcq = 50 ps
tsetup = 60 ps
thold = 70 ps
tpd = 35 ps
tcd = 25 ps
FAIL

## Slide 55: Example: Fixing Hold Time Violation
tpd =
tcd =
Check setup time constraints:
Tc > tpcq + tpd + tsetup
Tc >
fc =
Check hold time constraints:
tccq + tcd > thold ?
Add buffers to the short paths:
Timing Characteristics
tccq = 30 ps
tpcq = 50 ps
tsetup = 60 ps
thold = 70 ps
tpd = 35 ps
tcd = 25 ps

## Slide 56: Example: Fixing Hold Time Violation
tpd = 3 x 35 ps = 105 ps
tcd = 2 x 25 ps = 50 ps
Check setup time constraints:
Tc > tpcq + tpd + tsetup
Tc >
fc =
Check hold time constraints:
tccq + tcd > thold ?
Add buffers to the short paths:
Timing Characteristics
tccq = 30 ps
tpcq = 50 ps
tsetup = 60 ps
thold = 70 ps
tpd = 35 ps
tcd = 25 ps

## Slide 57: Example: Fixing Hold Time Violation
tpd = 3 x 35 ps = 105 ps
tcd = 2 x 25 ps = 50 ps
Check setup time constraints:
Tc > tpcq + tpd + tsetup
Tc > (50 + 105 + 60) ps = 215 ps
fc = 1/Tc = 4.65 GHz
Check hold time constraints:
tccq + tcd > thold ?
Add buffers to the short paths:
Timing Characteristics
tccq = 30 ps
tpcq = 50 ps
tsetup = 60 ps
thold = 70 ps
tpd = 35 ps
tcd = 25 ps
tpd
tpcq
tsetup

## Slide 58: Example: Fixing Hold Time Violation
tpd = 3 x 35 ps = 105 ps
tcd = 2 x 25 ps = 50 ps
Check setup time constraints:
Tc > tpcq + tpd + tsetup
Tc > (50 + 105 + 60) ps = 215 ps
fc = 1/Tc = 4.65 GHz
Check hold time constraints:
tccq + tcd > thold ?
Add buffers to the short paths:
Timing Characteristics
tccq = 30 ps
tpcq = 50 ps
tsetup = 60 ps
thold = 70 ps
tpd = 35 ps
tcd = 25 ps
Note: no change
to max frequency!

## Slide 59: Example: Fixing Hold Time Violation
tpd = 3 x 35 ps = 105 ps
tcd = 2 x 25 ps = 50 ps
Check setup time constraints:
Tc > tpcq + tpd + tsetup
Tc > (50 + 105 + 60) ps = 215 ps
fc = 1/Tc = 4.65 GHz
Check hold time constraints:
tccq + tcd > thold ?
(30 + 50) ps > 70 ps ?
Add buffers to the short paths:
Timing Characteristics
tccq = 30 ps
tpcq = 50 ps
tsetup = 60 ps
thold = 70 ps
tpd = 35 ps
tcd = 25 ps
tccq
tcd

## Slide 60: Example: Fixing Hold Time Violation
tpd = 3 x 35 ps = 105 ps
tcd = 2 x 25 ps = 50 ps
Check setup time constraints:
Tc > tpcq + tpd + tsetup
Tc > (50 + 105 + 60) ps = 215 ps
fc = 1/Tc = 4.65 GHz
Check hold time constraints:
tccq + tcd > thold ?
(30 + 50) ps > 70 ps ?
Add buffers to the short paths:
Timing Characteristics
tccq = 30 ps
tpcq = 50 ps
tsetup = 60 ps
thold = 70 ps
tpd = 35 ps
tcd = 25 ps
PASS

## Slide 61: Clock Skew
To make matters worse, clocks have delay too!
  The clock does not reach all parts of the chip at the same time!
Clock skew: time difference between two clock edges
Clock Source
Point A
Point B
clock skew
A
B
Long, slow
clock path
CLOCK
SOURCE

## Slide 62: Clock Skew Example
Example of the Alpha 21264 clock skew spatial distribution
P. E. Gronowski+, "High-performance Microprocessor Design," JSSC’98.

## Slide 63: Clock Skew: Setup Time Revisited
Safe timing requires considering the worst-case skew
  Clock arrives at R2 before R1
  Leaves as little time as possible for the combinational logic
Tc > tpcq + tpd + tsetup + tskew
Signal must arrive at D2 earlier!
This effectively increases tsetup:
Tc > tpcq + tpd + tsetup, effective

## Slide 64: Clock Skew: Hold Time Revisited
tcd + tccq > thold + tskew
Safe timing requires considering the worst-case skew
  Clock arrives at R2 after R1
  Increases the minimum required delay for the combinational logic
Signal must arrive at D2 later!
This effectively increases thold:
thold
tskew
tcd
tccq
tcd + tccq > thold, effective

## Slide 65: Clock Skew: Summary
Skew effectively increases both tsetup and thold
  Increased sequencing overhead
  i.e., less useful work done per cycle
Designers must keep skew to a minimum
  Requires intelligent “clock network” across a chip
  Goal: clock arrives at all locations at roughly the same time
Source: Abdelhadi, Ameer, et al. "Timing-driven variation-aware nonuniform clock mesh synthesis." GLSVLSI’10.

## Slide 66: Part 3: Circuit Verification

## Slide 67: How Do You Know That A Circuit Works?
You have designed a circuit
  Is it functionally correct?
  Even if it is logically correct, does the hardware meet all timing constraints?
How can you test for:
  Functionality?
  Timing?
Answer: simulation tools!
  Formal verification tools (e.g., SAT solvers)
  HDL timing simulation (e.g., Vivado)
  Circuit simulation (e.g., SPICE)

## Slide 68: Testing Large Digital Designs
Testing can be the most time consuming design stage
  Functional correctness of all logic paths
  Timing, power, etc. of all circuit elements
Unfortunately, low-level (e.g., circuit) simulation is much slower than high-level (e.g., HDL, C) simulation
Solution: we split responsibilities:
  1) Check only functionality at a high level (e.g., C, HDL)
    (Relatively) fast simulation time allows high code coverage
    Easy to write and run tests
  2) Check only timing, power, etc. at low level (e.g., circuit)
    No functional testing of low-level model
    Instead, test functional equivalence to high-level model
      Hard, but easier than testing logical functionality at this level
Adapted from ”CMOS VLSI Design 4e”, Neil H. E. Weste and David Money Harris ©2011 Pearson

## Slide 69: Testing Large Digital Designs
We have tools to handle different levels of verification
  Logic synthesis tool guarantees equivalence of high-level logic and synthesized circuit-level description
  Timing verification tools check all circuit timings
  Design rule checks ensure that physical circuits are buildable
Our job as a logic designer is to:
  Provide functional tests for logical correctness of the design
  Provide timing constraints (e.g., desired operating frequency)
Tools and/or circuit engineers will decide if it can be built!
Adapted from ”CMOS VLSI Design 4e”, Neil H. E. Weste and David Money Harris ©2011 Pearson

## Slide 70: Part 4: Functional Verification

## Slide 71: Functional Verification
Goal: check logical correctness of the design
Physical circuit timing (e.g., tsetup/thold) is typically ignored
  May implement simple checks to catch obvious bugs
  We’ll discuss timing verification later in this lecture
There are two primary approaches
  Logic simulation (e.g., C/C++/Verilog test routines)
  Formal verification techniques
In this course, we will use Verilog for functional verification

## Slide 72: Testbench-Based Functional Testing
Testbench: a module created specifically to test a design
  Tested design is called the “device under test (DUT)”
Testbench
DUT
Inputs
Outputs
Test Pattern Generator
Output
Checking
Logic
Testbench provides inputs (test patterns) to the DUT
  Hand-crafted values
  Automatically generated (e.g., sequential or random values)
Testbench checks outputs of the DUT against:
  Hand-crafted values
  A “golden design” that is known to be bug-free

## Slide 73: Testbench-Based Functional Testing
A testbench can be:
  HDL code written to test other HDL modules
  Circuit schematic used to test other circuit designs
The testbench is not designed for hardware synthesis!
  Runs in simulation only
    HDL simulator (e.g., Vivado simulator)
    SPICE circuit simulation
  Testbench uses simulation-only constructs
    E.g., “wait 10ns”
    E.g., ideal voltage/current source
    Not suitable to be physically built!

## Slide 74: Common Verilog Testbench Types
Testbench | Input/Output Generation | Error Checking
Simple | Manual | Manual
Self-Checking | Manual | Automatic
Automatic | Automatic | Automatic

## Slide 75: Example DUT
We will walk through different types of testbenches to test a module that implements the logic function:
y = (b ∙ c) + (a ∙ b)
// performs y = ~b & ~c | a & ~b
module sillyfunction(input a, b, c,
output y);
wire b_n, c_n;
wire m1, m2;
not not_b(b_n, b);
not not_c(c_n, c);
and minterm1(m1, b_n, c_n);
and minterm2(m2, a, b_n);
or out_func(y, m1, m2);
endmodule

## Slide 76: Useful Verilog Syntax for Testbenching
module example_syntax();
reg a;
// like “always” block, but runs only once at sim start
initial
begin
a = 0; // set value of reg: use blocking assignments
#10; // wait (do nothing) for 10 ns
a = 1;
$display(“printf() style message!"); // print message
end
endmodule

## Slide 77: Simple Testbench

## Slide 78: Simple Testbench
module testbench1(); // No inputs, outputs
reg a, b, c; // Manually assigned
wire y; // Manually checked
// instantiate device under test
sillyfunction dut (.a(a), .b(b), .c(c), .y(y) );
// apply hardcoded inputs one at a time
initial begin
a = 0; b = 0; c = 0; #10; // apply inputs, wait 10ns
c = 1; #10; // apply inputs, wait 10ns
b = 1; c = 0; #10; // etc .. etc..
c = 1; #10;
a = 1; b = 0; c = 0; #10;
end
endmodule

## Slide 79: Simple Testbench: Output Checking
Most common method is to look at waveform diagrams
  Thousands of signals over millions of clock cycles
  Too many to just printf()!
https://www.xilinx.com/support/documentation/sw_manuals/xilinx13_2/ism_c_mxe_sim_step4.htm
Manually check that output is correct at all times
time

## Slide 80: Simple Testbench
Pros:
  Easy to design
  Can easily test a few, specific inputs (e.g., corner cases)
Cons:
  Not scalable to many test cases
  Outputs must be checked manually outside of the simulation
    E.g., inspecting dumped waveform signals
    E.g., printf() style debugging

## Slide 81: Self-Checking Testbench

## Slide 82: Self-Checking Testbench
module testbench2();
reg a, b, c;
wire y;
sillyfunction dut(.a(a), .b(b), .c(c), .y(y));
initial begin
a = 0; b = 0; c = 0; #10; // apply input, wait 10ns
if (y !== 1) $display("000 failed."); // check result
c = 1; #10;
if (y !== 0) $display("001 failed.");
b = 1; c = 0; #10;
if (y !== 0) $display("010 failed.");
end
endmodule

## Slide 83: Self-Checking Testbench
Pros:
  Still easy to design
  Still easy to test a few, specific inputs (e.g., corner cases)
  Simulator will print whenever an error occurs
Cons:
  Still not scalable to millions of test cases
  Easy to make an error in hardcoded values
    You make just as many errors writing a testbench as actual code
    Hard to debug whether an issue is in the testbench or in the DUT

## Slide 84: Self-Checking Testbench using Testvectors
Write testvector file
  List of inputs and expected outputs
  Can create vectors manually or automatically using an already verified, simpler “golden model” (more on this later)
Example file:
  $ cat testvectors.tv
  000_1
  001_0
  010_0
  011_0
  100_1
  101_1
  110_0
  111_0
  …
Format: input_output

## Slide 85: Testbench with Testvectors Design
Use a “clock signal” for assigning inputs, reading outputs
  Test one testvector each “clock cycle”
Apply input
on rising edge
Check outputs on falling edge
Clock cycle
Note: “clock signal” simply separates inputs from outputs
  Allows us to observe the inputs/outputs in waveform diagrams
  Not used for checking physical circuit timing (e.g., tsetup/thold)
  We’ll discuss circuit timing verification later in this lecture

## Slide 86: Testbench Example (1/5): Signal Declarations
module testbench3();
reg clk, reset; // clock and reset are internal
reg a, b, c, yexpected; // values from testvectors
wire y; // output of circuit
reg [31:0] vectornum, errors; // bookkeeping variables
reg [3:0] testvectors[10000:0];// array of testvectors
// instantiate device under test
sillyfunction dut(.a(a), .b(b), .c(c), .y(y) );
Declare signals to hold internal state
H&H Section 4.9, Example 4.39

## Slide 87: Testbench Example (2/5): Clock Generation
// generate clock
always // no sensitivity list, so it always executes
begin
clk = 1; #5; clk = 0; #5; // 10ns period
end

## Slide 88: Testbench Example (3/5): Read Testvectors into Array
// at start of test, load vectors and pulse reset
initial // Only executes once
begin
$readmemb("example.tv", testvectors); // Read vectors
vectornum = 0; errors = 0; // Initialize
reset = 1; #27; reset = 0; // Apply reset wait
end
// Note: $readmemh reads testvector files written in
// hexadecimal

## Slide 89: Testbench Example (4/5): Assign Inputs/Outputs
Apply {a, b, c} inputs on the rising edge of the clock
Get yexpected for checking the output on the falling edge
Rising/falling edges are chosen only by convention
  You can use any part of the clock signal
  Your H+H textbook uses this convention
// apply test vectors on rising edge of clk
always @(posedge clk)
begin
{a, b, c, yexpected} = testvectors[vectornum];
end

## Slide 90: Testbench Example (5/5): Check Outputs
always @(negedge clk)
begin
if (~reset) // don’t test during reset
begin
if (y !== yexpected)
begin
$display("Error: inputs = %b", {a, b, c});
$display(" outputs = %b (%b exp)",y,yexpected);
errors = errors + 1;
end
// increment array index and read next testvector
vectornum = vectornum + 1;
if (testvectors[vectornum] === 4'bx)
begin
$display("%d tests completed with %d errors",
vectornum, errors);
$finish; // End simulation
end
end
end

## Slide 91: Self-Checking Testbench with Testvectors
Pros:
  Still easy to design
  Still easy to test a few, specific inputs (e.g., corner cases)
  Simulator will print whenever an error occurs
  No need to change hardcoded values for different tests
Cons:
  May be error-prone depending on source of testvectors
  More scalable, but still limited by reading a file
    Might have many more combinational paths to test than will fit in memory

## Slide 92: Automatic Testbench

## Slide 93: Golden Models
A golden model represents the ideal circuit behavior
  Must be developed, and might be difficult to write
  Can be done in C, Perl, Python, Matlab or even in Verilog
For our example circuit:
module golden_model(input a, b, c,
output y);
assign y = ~b & ~c | a & ~b;// high-level abstraction
endmodule
Simpler than our earlier gate-level description
  Golden model is usually easier to design and understand
  Golden model is much easier to verify

## Slide 94: Automatic Testbench
The DUT output is compared against the golden model
Testbench
DUT
Inputs
Outputs
Check Equality
Golden Model
Test Pattern Generation
Challenge: need to generate inputs to the designs
  Sequential values to cover the entire input space?
  Random values?

## Slide 95: Automatic Testbench: Code
module testbench1();
... // variable declarations, clock, etc.
// instantiate device under test
sillyfunction dut (a, b, c, y_dut);
golden_model gold (a, b, c, y_gold);
// instantiate test pattern generator
test_pattern_generator tgen (a, b, c, clk);
// check if y_dut is ever not equal to y_gold
always @(negedge clk)
begin
if(y_dut !== y_gold)
$display(...)
end
endmodule

## Slide 96: Automatic Testbench
Pros:
  Output checking is fully automated
  Could even compare timing using a golden timing model
  Highly scalable to as much simulation time as is feasible
    Leads to high coverage of the input space
  Better separation of roles
    Separate designers can work on the DUT and the golden model
    DUT testing engineer can focus on important test cases instead of output checking
Cons:
  Creating a correct golden model may be (very) difficult
  Coming up with good testing inputs may be difficult

## Slide 97: However, Even with Automatic Testing…
How long would it take to test a 32-bit adder?
  In such an adder there are 64 inputs = 264 possible inputs
  If you test one input in 1ns, you can test 109 inputs per second
    or 8.64 x 1014 inputs per day
    or 3.15 x 1017 inputs per year
  we would still need 58.5 years to test all possibilities
Brute force testing is not feasible for most circuits!
  Need to prune the overall testing space
  E.g., formal verification methods, choosing ‘important cases’
Verification is a hard problem

## Slide 98: Part 5: Timing Verification

## Slide 99: Timing Verification Approaches
High-level simulation (e.g., C, Verilog)
  Can model timing using “#x” statements in the DUT
  Useful for hierarchical modeling
    Insert delays in FF’s, basic gates, memories, etc.
    High level design will have some notion of timing
  Usually not as accurate as real circuit timing
Circuit-level timing verification
  Need to first synthesize your design to actual circuits
    No one general approach- very design flow specific
    Your FPGA/ASIC/etc. technology has special tool(s) for this
      E.g., Xilinx Vivado (what you’re using in lab)
      E.g., Synopsys/Cadence Tools (for VLSI design)

## Slide 100: The Good News
Tools will try to meet timing for you!
  Setup times, hold times
  Clock skews
  …
They usually provide a ‘timing report’ or ‘timing summary’
  Worst-case delay paths
  Maximum operation frequency
  Any timing errors that were found

## Slide 101: The Bad News
The tool can fail to find a solution
  Desired clock frequency is too aggressive
    Can result in setup time violation on a particularly long path
  Too much logic on clock paths
    Introduces excessive clock skew
  Timing issues with asynchronous logic
The tool will provide (hopefully) helpful errors
  Reports will contain paths that failed to meet timing
  Gives a place from where to start debugging
Q: How can we fix timing errors?

## Slide 102: Meeting Timing Constraints
Unfortunately, this is often a manual, iterative process
  Meeting strict timing constraints (e.g., high performance designs) can be tedious
Can try synthesis/place-and-route with different options
  Different random seeds
  Manually provided hints for place-and-route
Can manually optimize the reported problem paths
  Simplify complicated logic
  Split up long combinational logic paths
  Recall: fix hold time violations by adding more logic!

## Slide 103: Meeting Timing Constraints: Principles
Let’s go back to the fundamentals
Clock cycle time is determine by the maximum logic delay we can accommodate without violating timing constraints
Good design principles
  Critical path design: Minimize the maximum logic delay
     Maximizes performance
  Balanced design: Balance maximum logic delays across different parts of a system (i.e., between different pairs of flip flops)
     No bottlenecks + minimizes wasted time
  Bread and butter design: Optimize for the common case, but make sure non-common-cases do not overwhelm the design
     Maximizes performance for realistic cases

## Slide 104: Lecture Summary
Timing in combinational circuits
  Propagation delay and contamination delay
  Glitches
Timing in sequential circuits
  Setup time and hold time
  Determining how fast a circuit can operate
Circuit Verification
  How to make sure a circuit works correctly
  Functional verification
  Timing verification

## Slide 105: Digital Design & Computer Arch. Lecture 8: Timing and Verification
Prof. Onur Mutlu
ETH Zürich
Spring 2020
13 March 2020